## Slide 1: Micro Surfacing In Your Neighborhood

## Slide 2
Part of a family of asphalt maintenance treatments used worldwide since
the 1930’s
Slurry surfacing systems used in the US since the 60’s
Slurry Pavers has been applying them for more than 50 years

## Slide 3
Blend of emulsified asphalt, fine aggregate, mineral filler, water and latex polymers
Mixed and spread in a mobile operation as thin wearing surface
Extends the life of pavement in upwards of 8 years or longer.

## Slide 4
Micro Surfacing vs. traditional asphalt resurfacing

## Slide 5
PCI Rating Scale
A = 85-100
B = 70-84
C = 55-69
D = 40-54
F = 0-39
Courtesy of roadresource.org

## Slide 8: A Tale of Two Townships

## Slide 9: 2004 Mill and Fill 2.5” Hot Mix Asphalt

## Slide 10
2004 Mill and Fill 2.5” Hot Mix Asphalt
2010 Crack Fill and Micro Surfacing
Photo taken in 2014

## Slide 13
Project Notification mailed well in advance of all work commencing
Signs and Notices several days before slurry application begins
No Parking signs posted in advance
Community groups and website updated throughout the project

## Slide 14: Crack Sealing
Cracks 1/4 inch and greater filled
Quick-moving operation, parking affected need-only
Work zone protected by flaggers
Generally unintrusive

## Slide 15: Patching
Localized failures repaired with plant mix asphalt
Includes potholes, utility cuts, wide cracks, minor “alligatoring”
Localized parking restrictions

## Slide 16: Micro Surfacing
On the day work begins Traffic Control crew arrives
Cones put out, manhole and utility covers protected
TIP: Work will be performed today.

## Slide 17: Micro Surfacing
Some intersections taped off
Roadway swept prior to resurfacing

## Slide 18: Micro Surfacing
Brown when initially placed
Water evaporates and surface turns black
Coned off, flaggers
Traffic-ready in 1 to 2 hours
TIP: Do not cross brown Micro Surfacing

## Slide 19: Micro surfacing
Lanes will be clearly defined by traffic cones
When in doubt, the darker lane will be the travel lane
Drive conservatively

## Slide 20: Micro Surfacing
Some cul-de-sacs may need to be done all at once
Residents in the circle will be notified to make arrangements to move vehicles if necessary
TIP: Crew will notify residents if so

## Slide 21
Surface "fines" ravel off during wear-in and curing
Streets are swept about two weeks after treatment, sanding swept earlier
Monitored for several weeks and then inspected to ensure everything is complete

## Slide 22: Cooperation is Key!
Please follow direction from traffic control
Pay attention to road signs

## Slide 23
New Asphalt surfaces can scuff
High surface temps soften every type of new asphalt
Drive conservatively and avoid sitting still while turning wheel
Most will blend in with time and traffic

## Slide 24
Micro Surface or Hot Mix Asphalt?

## Slide 25
Homeowners' New Hot Mix Asphalt and Asphalt Pavement Sealer

## Slide 26
www.neighborhoodslurry.com

## Slide 27: Thank you.